## Slide 1: 计算机网络 复习
计算机网络与信息安全研究室
徐敬东 张建忠
xujd@nankai.edu.cn
zhangjz@nankai.edu.cn

## Slide 2
对等层通信，执行相关协议
路由器
应用层
传输层
网络层
接口层
应用层
传输层
网络层
接口层
网络层
接口层
接口层
网络层
接口层
接口层
路由器
TCP/IP体系结构
构建物理网络

## Slide 3
接口层基础：物理网、接口层功能（物理层和数据链路层）
局域网体系结构（IEEE 802）与组网方法（共享、交换）
局域网编址（48位地址）与ARP协议
链路层差错控制（CRC校验）
交换式以太网（工作机制、地址学习）
无线局域网（介质访问控制方法CSMA/CA，RTS/CTS)
第五章 接口层原理与协议

## Slide 4
对等层通信，执行相关协议
路由器
应用层
传输层
网络层
接口层
应用层
传输层
网络层
接口层
网络层
接口层
接口层
网络层
接口层
接口层
路由器
TCP/IP体系结构
互联异构的物理网络

## Slide 5
第四章 网络层协议
网络层功能
IP协议（数据面）
  IPv4数据包格式和地址
  IPv4数据包转发
  IPv4地址问题及解决策略（CIDR、NAT）
  IPv6基础
ICMP协议（Tracert）
路由算法
  链路状态算法
  距离向量算法
互联网路由协议：RIP, OSPF, BGP
软件定义网络（SDN）
控制面

## Slide 6
对等层通信，执行相关协议
路由器
应用层
传输层
网络层
接口层
应用层
传输层
网络层
接口层
网络层
接口层
接口层
网络层
接口层
接口层
路由器
TCP/IP体系结构
不可靠服务基础上的可靠机制与复用

## Slide 7
第三章 传输层协议
传输层需要解决的基本问题
TCP/IP体系结构中传输层协议与服务
用户数据报协议（UDP）
可靠数据传输
传输控制协议（TCP）（可靠、流控、连接管理）
理解网络拥塞
TCP拥塞控制机制

## Slide 8
对等层通信，执行相关协议
路由器
应用层
传输层
网络层
接口层
应用层
传输层
网络层
接口层
网络层
接口层
接口层
网络层
接口层
接口层
路由器
TCP/IP体系结构
可靠和不可靠服务基础上的应用协议

## Slide 9
第二章 应用层协议及网络编程
应用协议与进程通信模型
传输层服务对应用的支持
Socket编程
域名系统
电子邮件服务与协议
文件传输服务与协议
Web服务与HTTP协议
内容分发网络CDN
动态自适应流媒体协议DASH

## Slide 10
第一章 概述
计算机网络构成及基本概念
Internet发展历程
Internet的核心与边缘
TCP/IP网络体系结构
Web服务器访问示例
理解Internet总貌和TCP/IP网络体系结构

## Slide 11
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 12
ISP network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 13
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 14
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server

## Slide 15
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 16
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Internet, routed (tables created by RIP, OSPF and/or BGP routing protocols) to DNS server
demux’ed to DNS server
DNS server replies to client with IP address of www.google.com
ISP network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 17
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 18
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 19
请将试题的作答写在答题卡的相应位置上。由于采用机器阅卷，并使用流水方式，如不在正确的位置上，机器不会正确显示你的作答。例如，你在作答第6题时，你必须将你的作答写在答题纸第6题的方框内，不要超出第6题的方框。我们在判第6题时，看不到你答题卡的其他位置上的内容
答题时请使用黑色的油笔或水笔，不要使用蓝色或红色的笔，更不能使用铅笔
答题卡不能折，特别要注意不能折角，以防答题卡扫不进电脑
答题卡有正反面时，请不要在禁答区域上写字。在禁答区域写字，有可能对另一面的涂卡造成影响
答题卡上需要在每一页上写明你的姓名和学号。另外，学号一定要涂正确，以保证机器识别。
考试的题目顺序不是按照难易程度排列的，请同学们在答题时注意。
期末考试注意事项